## Slide 1
晚晴：一句话如何变成一次可执行提醒
ROROLEE-Basic｜实线＝代码可追踪主链路 · 虚线＝结构化提醒端到端待验证
主办方提供
团队配置
团队自主开发
01 真实输入
02 ESP32 设备 + 能力层
03 连接方式
04 Agent / Tool 智能层
GPIO /
I²S
0x40 ↑
TTS/0x70 ↓
HTTPS
NDJSON
下行：Agent / 到点提醒 → App → BLE → ESP32
虚线：0x70 reminder 专属 UI / 三连振（App 待验）
BOOT（GPIO0）
按住说话，松开结束
ES7210 双麦
16 kHz PCM
音量±（39 / 40）
BQ27220 电量/充电
ROROLEE-Basic
提供
ESP32-S3 · ES7210 / ES8311 · SH8501 · BQ27220 · 震动马达
板级固件 / 0x70
自研
PTT 采集 / 音频队列 · 11 状态表情
触觉模式 · 电量轮询 · JSON → Board 动作
agent_link SDK
提供
voice ↑ · audio / custom ↓
App + roro
提供
BLE 网关 · ASR / TTS
MQTT / 云中继
Shim + Bridge
自研
PTY 兼容 · Session / Turn
NDJSON → 回复
链路配置
配置
BLE v1 · MCP 注册
TiDB Agent Stack · 晚晴 Agent
团队配置
qwen3.7-plus · Session 上下文 · Scheduler
Prompt：适老语气 / 时间解析 / 最小追问
Skill：主链路未单独启用（Prompt + MCP）
MCP · 5 Tools
自研
create_task / note / query
complete / delay
SQLite
自研
任务 / 备忘
状态持久化
reminder-pusher：Scheduler → MQTT → App
自研
05 实际输出（回到同一台 ROROLEE-Basic）
声音｜ES8311 播放 16 kHz PCM TTS
屏幕｜SH8501 显示 11 状态表情
触觉｜连接 / 上传 / 错误 / 提醒模式
后续｜SQLite 保存；Scheduler 到点触发
关键硬件能力映射：Agent / Tool → SDK → 设备动作
Agent / Tool 决策
SDK / 链路
具体设备动作
回答 / TTS
App → L2CAP → on_audio_out
ES8311 播放 + Speaking 表情
Scheduler 到点
pusher → MQTT / App → BLE
TTS；0x70 → Reminder + 振动*
调节音量
0x70 on_custom
SetVolumePercent → ES8311
* 当前 AMOLED 输出为表情动画，ShowText 仅写日志；BOOT 语音上行已实现但真机全链路待验；结构化 reminder 的 App 转发待验，普通文本/TTS 为可靠兜底。
Notes: [Sources]
- /Users/nibelung/Desktop/VentureD/Agent_link/boards/rorolee-basic/rorolee_basic.cc
- /Users/nibelung/Desktop/VentureD/Agent_link/boards/rorolee-basic/config.h
- /Users/nibelung/Desktop/VentureD/Agent_link/main/app_main.cpp
- /Users/nibelung/Desktop/VentureD/Agent_link/boards/common/device_protocol.cc
- /Users/nibelung/Desktop/VentureD/Agent_link/components/agent_link/README.md
- /Users/nibelung/Desktop/VentureD/wanqing/bridge/claude-bridge
- /Users/nibelung/Desktop/VentureD/wanqing/bridge/reminder-pusher
- /Users/nibelung/Desktop/VentureD/wanqing/backend/mcp_server.py
- /Users/nibelung/Desktop/VentureD/wanqing/backend/models/database.py
- /Users/nibelung/Desktop/VentureD/wanqing/prompts/system_prompt.md
- /Users/nibelung/Desktop/VentureD/wanqing/docs/ble_protocol_v1.md